## Slide 1: CS683 Project Proposal LoGO: Combining Local Deltas and Global Offsets for Data Prefetching Mradul Sonkar 23b0980@iitb.ac.in

## Slide 2: Problem statement
Offset-based prefetchers learn a fixed distance (an offset or delta) between accesses and prefetch addr + offset. They are cheap (a few KB) and effective on regular access patterns.
  Global offset (BOP): learns one best offset for the whole program. It is simple and timely, but it mixes patterns from different load instructions (IPs) and loses accuracy when IPs behave differently.
  Local per-IP delta (Berti): learns deltas per IP and is very accurate. But it issues no prefetch for IPs where no delta reaches confidence, such as cold IPs, IPs with few accesses, or patterns that only show up across IPs.
Problem: neither family covers both cases. The coverage that Berti leaves on low-confidence IPs might be recovered by a global offset, without giving up Berti's accuracy.
Question: can a lightweight per-IP selector between the local delta and the global offset beat both, at small extra storage?

## Slide 3: Prior Works
Sandbox (Pugsley et al., HPCA'14)
BOP, Best-Offset (Michaud, HPCA'16)
MLOP (Shakerinava et al., DPC-3'19)
IPCP (Pakalapati & Panda, ISCA'20)
Berti (Navarro-Torres et al., MICRO'22)

## Slide 4: Goal of the Project
Goal: design and evaluate LoGO, which extends Berti at L1D with a global best-offset learner (in the style of BOP) and a per-IP selector:
  If an IP has a confident Berti delta, use it.
  Otherwise, fall back to the global offset, but only while that offset's measured accuracy stays above a threshold.
Target: higher coverage than Berti, higher accuracy than BOP, and less than 1 KB of extra storage.
Simulator: ChampSim
During the project, I won’t be relying on GenAI tools to do my work. I will myself understand the existing solutions to the problem, try to find the gaps and come up with strategies that help me improve the benchmarks.

## Slide 5: Plan for checkpoint-I
Experiments:
  Infrastructure: port Berti and BOP to the current ChampSim, then check the ports against the trends reported in their papers.
  Baseline characterization: run all baselines on every trace (50M instructions warmup, 200M simulated). Collect IPC, accuracy, coverage and late prefetches.
  Per-IP coverage analysis (key experiment): instrument Berti to log, for each IP:
    how many accesses it makes
    whether it ever reaches a confident delta
    how many misses come from IPs with no confident delta
    This measures how much the gap is worth.
  Global offset potential: on those uncovered misses, measure how often BOP's best offset would have predicted them correctly.
  Sensitivity: sweep DRAM bandwidth and L1D/L2 sizes to see how each prefetcher holds up.

## Slide 6: Plan for checkpoint-I
Expected insights:
  On irregular or multi-IP workloads (GAP, omnetpp, xalancbmk), a large fraction of L1D misses come from IPs where Berti stays silent.
  A global offset predicts part of those misses correctly. That would justify the fallback.
  Without an accuracy filter, the fallback would add DRAM traffic. That is why the selector is gated on accuracy.
Anything else: if the analysis shows the gap is small, switch to the backup idea, bandwidth-aware degree control for Berti, using the same infrastructure.

## Slide 7: Plan for checkpoint-II
Implement LoGO:
  add a global offset learner (recent-requests table plus offset score table) alongside Berti's tables
  add a mode bit per IP (Berti delta or global fallback)
  add an accuracy counter for fallback prefetches, using a "prefetched" bit on cache lines to count useful ones
Evaluate:
  single-core: LoGO against Berti, BOP and IP-stride across all traces (geometric-mean speedup, plus per-workload results)
  4-core mixes: weighted speedup and DRAM traffic