## Slide 1: CS683 Project Proposal LoGO: Combining Local Deltas and Global Offsets for Data Prefetching Mradul Sonkar 23b0980@iitb.ac.in

## Slide 2: Problem statement
1. Offset-based prefetchers learn a fixed distance (an offset or delta) between accesses and prefetch addr + offset. They are cheap (a few KB) and effective on regular access patterns.
- Global offset (BOP): learns one best offset for the whole program. It is simple and timely, but it mixes patterns from different load instructions (IPs) and loses accuracy when IPs behave differently.
- Local per-IP delta (Berti): learns deltas per IP and is very accurate. But it issues no prefetch for IPs where no delta reaches confidence, such as cold IPs, IPs with few accesses, or patterns that only show up across IPs.
Problem: neither family covers both cases. The coverage that Berti leaves on low-confidence IPs might be recovered by a global offset, without giving up Berti's accuracy. Question: can a lightweight per-IP selector between the local delta and the global offset beat both, at small extra storage?

## Slide 3: Prior Works
Sandbox (Pugsley et al., HPCA'14)
BOP, Best-Offset (Michaud, HPCA'16)
MLOP (Shakerinava et al., DPC-3'19)
IPCP (Pakalapati & Panda, ISCA'20)
Berti (Navarro-Torres et al., MICRO'22)

## Slide 4: Goal of the Project
Goal:design and evaluate LoGO, which extends Berti at L1D with a global best-offset learner (in the style of BOP) and a per-IP selector:
If an IP has a confident Berti delta, use it.
Otherwise, fall back to the global offset, but only while that offset's measured accuracy stays above a threshold.
Target:higher coverage than Berti, higher accuracy than BOP, and less than 1 KB of extra storage.
Simulator:ChampSim
During the project, I won’t be relying on GenAI tools to do my work. I will myself understand the existing solutions to the problem, try to find the gaps and come up with strategies that help me improve the benchmarks.

## Slide 5: Plan for checkpoint-I
What experiments will you perform and why?
What insights you expect to build your proposal?
Anything else

## Slide 6: Plan for checkpoint-II
More closer after checkpoint-I